## Slide 1
Lab 10 – ViewPoint
Navisworks API Training

## Slide 2: Agenda
Viewpoint
Manipulate Camera
Saved Viewpoint
Manipulate Saved Viewpoint

## Slide 3: Overview
How eyes look at the modal
Based on graphics theory
Store properties to configure the viewpoint, e.g.
  Camera
    Position
    View direction
    Rotation
  Linear Speed
  Angular Speed

## Slide 4: Saved Viewpoint
Preset views of the model
Enable to jump to viewpoints without having to navigate each time to reach an item
  Saved Viewpoint: preset viewpoint
  Folder: contains saved viewpoints or sub-folder
  Animation: viewpoint animation clip (each element is a saved viewpoint)

## Slide 5: .NET API
Viewpoint
  Anonymous Viewpoint
  Object to manipulate camera
Move camera
  Position/PointAt/ AlignUp
Rotate camera:
  ViewPoint.Rotation - Rotation3D
  rotation in 3D space defined as a quaternion*. Some direct methods for Quaternion are provided
Other properties
  NearPlaneDistance,FarPlaneDistance,LinearSpeed,AngularSpeed
Current viewpoint
  DocumentCurrentViewpoint

## Slide 6: Move Camera
// move camera along X+ with value 10
  Document oDoc = Autodesk.Navisworks.Api.Application.ActiveDocument;
  // make a copy of current viewpoint
  Viewpoint oCurrVCopy = oDoc.CurrentViewpoint.CreateCopy();
  // move to the new position
  Point3D newPos = new Point3D(oCurrVCopy.Position.X + 10 , oCurrVCopy.Position.Y,
  oCurrVCopy.Position.Z);
  oCurrVCopy.Position = newPos;
  // update current viewpoint with the copy one
  oDoc.CurrentViewpoint.CopyFrom(oCurrVCopy);

## Slide 7: Rotation - Euler Angles
Euler Angles
rotates around local axes
Order important! 3D non-commutative
Issues:
  No easy concatenation of rotations
  Still has interpolation problems
  Can lead to gimbal lock
Easy to understand, challenge to algorism

## Slide 8: Rotation - Quaternion
Created as extension to complex numbers
•Unit represents 3D rotation
e.g. if want to rotate 90°around z-axis
Notes: e.g. *: see more about Quaternion at http://en.wikipedia.org/wiki/Quaternion
http://www.essentialmath.com/GDC2012/GDC2012_JMV_Rotations.pdf

## Slide 9: Rotation3D
A rotation in 3D space defined as a quaternion.
A rotation is current quaternion multiplies incremental quaternion (based on axis and angle)
A,B,C,D
  The components of the quaternion
ToAxisAndAngle
  Calculates an axis and angle representation of this rotation

## Slide 10: Rotate Camera
//rotate camera around Z axis with value 45 degree
Document oDoc = Autodesk.Navisworks.Api.Application.ActiveDocument;
// Make a copy of current viewpoint
Viewpoint oCurrVCopy = oDoc.CurrentViewpoint.CreateCopy();
// Get the axis and angle from the current Quaternion
AxisAndAngleResult oAA = oCurrVCopy.Rotation.ToAxisAndAngle();
UnitVector3D oAxis = oAA.Axis;
double oldangle = oAA.Angle;
/
/ set the axis we will rotate around (0,0,1)
UnitVector3D odeltaA = new UnitVector3D(0, 0, 1);
// Create delta of Quaternion: axis is Z, angle is 45 degree
Rotation3D delta = new Rotation3D(odeltaA, 3.14/4);
// multiply the current Quaternion with the delta , get the new Quaternion
oCurrVCopy.Rotation = Multiply(oCurrVCopy.Rotation, delta);
// Update current viewpoint
oDoc.CurrentViewpoint.CopyFrom(oCurrVCopy);
Notes: .NET API does not provide Multiply methods for Quaternion. We could write it out ourselves.

## Slide 11: Saved Viewpoint
Document.SavedViewpoints
  Saved viewpoints collection
SavedViewpoint
  Saved viewpoint
Derives from GroupItem
  saved viewpoint
  folder – FolderItem
  animation clips - SavedViewpointAnimation
SavedViewpoints.CurrentSavedViewpoint
  The saved viewpoint is currently applied in the scene
  any view changes manually will cause it be anonymous viewpoint

## Slide 12: Demo: Iterate Saved Viewpoints
Document oDoc = Autodesk.Navisworks.Api.Application.ActiveDocument;
// iterate the collection of saved viewpoints
foreach (SavedItem oSVP in oDoc.SavedViewpoints.Value) {
if (oSVP.IsGroup) // if it is a folder/animation group
recurs(oSVP);
else {
    // Access the properties of the saved viewpoint
    // e.g. the viewpoint oSVP.ViewPoint
}
}
// help function to recurs
private void recurs(SavedItem oFolder)
{
foreach (SavedItem oSItem in ((GroupItem)oFolder).Children) {
if (oSItem.IsGroup)
recurse(oSItem);
if (oSItem is SavedViewpoint) {
SavedViewpoint oSVPt = oSItem as SavedViewpoint;
// Access the properties of the saved viewpoint
// oSVP.DisplayName
}
if (oSItem is SavedViewpointAnimationCut) {
SavedViewpointAnimationCut oSVCut = oSItem as SavedViewpointAnimationCut;
// Access the properties of the saved viewpoint
// oSVP.DisplayName
}
}
}

## Slide 13: Related Methods of Saved Viewpoints
SavedViewpoints.RootItem
  Top level item, root folder, invisible in UI
SavedViewpoints.AddCopy / InsertCopy
  Add a new item to collection with the copy of the new object
  Add specific item, or folder
  New object ≠ New item !
SavedViewpoints.Move
  Move item from one group (or root folder) to another
SavedViewpoints.ReplaceWithCopy
  Replace item at given index within Value with a copy of item

## Slide 14: Demo: Create Saved Viewpoint
// Create a saved viewpoint with current viewpoint
SavedViewpoint oNewViewPt1 = new SavedViewpoint(oDoc.CurrentViewpoint.ToViewpoint());
oNewViewPt1.DisplayName = “MySavedView1";
// Create a viewpoint for the second saved viewpoint
Viewpoint oNewVP = new Viewpoint();
// Based on the current viewpoint, move camera along X+ with value 10
oNewVP = oDoc.CurrentViewpoint.ToViewpoint().CreateCopy();
Point3D oNewPos = new Point3D(oNewVP.Position.X + 10,
oNewVP.Position.Y,
oNewVP.Position.Z);
oNewVP.Position = oNewPos;
// Create the saved viewpoint with the new viewpoint
SavedViewpoint oNewViewPt2 = new SavedViewpoint(oNewVP);
oNewViewPt2.DisplayName = " MySavedView2";
// Add the saved viewpoints to the collection
oDoc.SavedViewpoints.AddCopy(oNewViewPt1);
oDoc.SavedViewpoints.AddCopy(oNewViewPt2);

## Slide 15: Demo: Create Folder of Saved Viewpoints
Document oDoc = Autodesk.Navisworks.Api.Application.ActiveDocument;
DocumentSavedViewpoints oSavePts = oDoc.SavedViewpoints;
// if there are more than two saved viewpoints available
if (oSavePts.RootItem.Children.Count > 2)
{
// get the first saved viewpoint
SavedViewpoint oViewPt1 = (SavedViewpoint)oSavePts.RootItem.Children[0];
// get the second saved viewpoint
SavedViewpoint oViewPt2 = (SavedViewpoint)oSavePts.RootItem.Children[1];
// create a new folder
FolderItem oFolder = new FolderItem();
oFolder.DisplayName = " NewFolder";
//add the two saved viewpoints to the folder
oFolder.Children.Add(oViewPt1);
oFolder.Children.Add(oViewPt2);
//add folder to the collection of saved viewpoints.
oDoc.SavedViewpoints.AddCopy(oFolder);
}
Notes: I did not find a way to create animation group and animation cut.

## Slide 16: Demo: Move Saved Viewpoint to Folder
Document oDoc = Autodesk.Navisworks.Api.Application.ActiveDocument;
//get document part: SavedViewpoints
DocumentSavedViewpoints oSavePts = oDoc.SavedViewpoints;
//new object
FolderItem oFolderCopy = new FolderItem();
oFolderCopy.DisplayName = "NewFolder";
//insert the new object to saved viewpoints collection as a copy in index 0
oDoc.SavedViewpoints.InsertCopy(oSavePts.RootItem, 0, oFolderCopy);
//this is the item that really resides in the collection
FolderItem oRealFolder = (FolderItem)oSavePts.RootItem.Children[0];
//move first and second saved viewpoints of top level to the new folder
oSavePts.Move(oSavePts.RootItem, 0, oRealFolder, 0);
oSavePts.Move(oSavePts.RootItem, 1, oRealFolder, 0);

## Slide 17: Exercise
Create a plugin
rotate camera around (1,1,1) with angle 45 degree and save to saved viewpoint